## Slide 1: pocket_sdr.py help
Command Buttons
Page Tabs:
Tabs to switch current page
Status Bar:
Status info or error message for the receiver
: Start the receiver
: Stop the receiver
: Show Input Options dialog
: Show Output Options dialog
: Show Signal Options dialog
: Show System Options dialog
: Show Help dialog
: Exit the receiver
Start
Stop
Input...
Output...
Signal...
System...
Help
Exit
Receiver Time:
Elapsed time since the receiver started (s)
Initial Window
ver. 0.14 2025-03-20

## Slide 2: Receiver Page
Receiver Status Panel
Receiver Time:
Elapsed time since the receiver started
Input Source:
IF data source (RF_Frontend or IF_Data)
IF Data Fmt/# RF CH:
IF data format *3 and number of RF CHs
LO Frequencies:
Local oscillator frequencies for each RF CH (MHz)
Sampling:
IF data sampling type for each RF CH
(I or IQ)
Sampling Rate:
IF data sampling rate (Msps)
# BB CH Locked/All:
Number of BB CHs tracked and all
IF Data Rate:
IF data transfer rate (MB/s)
IF Data Buffer Usage:
Receiver internal IF data buffer usage rate (%)
Time (GPST):
PVT Solution time in GPST
Solution Status:
PVT Solution status (- or FIX)
Latitude, Longitude and Altitude:
PVT Solution latitude/ longitude (deg) and ellipsoidal height (m)
# Sats Used / All:
Number of used satellites for PVT and all satellites with OBS data
Solution Latency:
PVT Solution latency (s)
# PVT Solutions:
Total count of PVT solutions
# OBS/NAV Data:
Total count of OBS and NAV data
IF Data Log:
Recorded size of IF Data log (MB)
System Selection for Skyplot and C/N0 Plot
Output Status Indicators
for PVT solution, OBS/NAV data, receiver log and IF data log
Orange: waiting for connection
Green: data OK
Light-Green: data active
Red: error
White: no output
Satellite Positions in Skyplot *1 *2
* 1 GNSS System Color:
Green: GPS
Orange: GLONASS
Magenta: Galileo
Blue: QZSS
Red: BeiDou
Blue-Green: NavIC
Grey: SBAS
White or light-color:
unused satellites for solution
Signal C/N0 (dB-Hz) Plot for Each Satellite and Signals (stacked) *1 *2
Number of used satellites and all satellites with OBS data
*2 Satellite ID complies with RINEX convention
*3 INT8 (int8 I-sampling), INT8X2 (interleaved-int8 IQ-sampling), RAW8, RAW16 or RAW32 (Pocket SDR FE 2CH, 4CH or 8CH raw format)

## Slide 3: RF CH Page
Power Spectral Density Plot (Spectral Analyzer) for each RF CH
RF CH
Selection:
ALL, 1, 2, ..., 8, 1-4 or 5-8
Carrer-Frequency Marks for each GNSS Signal
Local Oscillator
Frequency
Sampling Type (I or IQ) and number of sample bits
IF Filter
Bandwidth
Sampling Rate
IF Filter Bandwidth and order Selection *1 *2
LNA Gain Selection *1
Averaging Time Selection for Power Spectral Density and Histogram
Histogram for IF Data Sample Values (I-sample and Q-sample)
Average and Standard Deviation of Sample Values
*1 Only valid for RF_Frontend Input, *2 Only valid for IQ-sampling
Link to GNSS Signal Band Table

## Slide 4: BB CH Page
RF CH
Selection:
ALL, 1, 2, ..., 8
GNSS System Selection:
ALL, GPS, GLONASS, ...
BB CH State Selection:
LOCK or ALL
Internal IF Data
Buffer Usage Rate in %
BB CH No Searching Signal
Number of Locked and All BB CHs
Status for each BB CH:
CH
RF
SAT
SIG
PRN
LOCK
C/N0
(dB-Hz)
COFF
DOP
ADR
SYNC
#NAV
#ERR
#LOL
FEC
: BB CH no
: Assigned RF CH no for BB CH
: Satellite ID
: Signal ID
: PRN number or FCN for
GLONASS FDMA signal
: Continuous lock time (s)
: Signal C/N0 (dB-Hz)
: Signal C/N0 Bar (20-50 dB-Hz)
: Code offset (ms)
: Doppler frequency (Hz)
: Accumulated Doppler range
(cycle)
: Synchronization status
: Decoded subframe or message
count
: NAV data error count
: Loss-of-lock count
: Number of error bits corrected
by FEC (-1: correction unable)
Synchronization Status:
S : Secondary code sync
B : NAV symbol (bit) sync
F : Subframe or message sync
R : Polarity of subframe or
message sync (R: reversed)
Link to GNSS Signal Table

## Slide 5: Correlator Page
BB CH
Selection *1:
1, 2, 3, ...
Satellite ID, Signal ID and Lock Time of BB CH
Correlation
Plot
X-axis: code offset (ms)
Y-axis: correlations
(I * sign(IP), sqrt(I2 + Q2) or sqrt(sum(I2 + Q2))) *2
Large dots:
correlator positions for
VE, E, P, L and VL *3
Constellation
Plot
X-axis: IP-correlation
Y-axis: QP-correlation
Large dot:
current correlation
Correlation
History Plot
X-axis: receiver time (s)
Y-axis: IP or QP-correlation
C/N0, code offset, Doppler Frequency, accumulated Doppler range, synchronization status, decoded subframe or message count
Correlation Plot Type Selection
Time Span Selection for Correlation History or Constellation Plot
Y-axis Range Selection
*1 BB CH can be selected by clicking BB CH Status row in BB CH Page
*2 Integration time is based on non-coherent integration time for DLL
*3 VE and VL are only shown in case of BOC-modulation and Bump-Jump enabled

## Slide 6: Satellites Page
Status for each Satellite:
SAT
FCN
PVT
OBS
EPH
SVH
AZ
EL
SIG1
C/N0
SIG2
C/N0
SIG3
C/N0
...
: Satellite ID
: Frequency channel no (FCN) for
GLONASS FDMA signals
: Satellite used in PVT solution or
not
: Satellite L1 OBS data availability
: Satellite ephemeris availability
: Satellite health flag in
ephemeris (HEX)
: Azimuth angle (deg)
: Elevation angle (deg)
: Signal 1 ID
: C/N0 of signal 1 (dB-Hz)
: Signal 2 ID
: C/N0 for signal 2 (dB-Hz)
: Signal 3 ID
: C/N0 for signal 3 (dB-Hz)
...
Orange: unhealthy satellite
Grey: unused satellite for PVT solution
System Selection
Number of satellites used for PVT solution, number of satellites tracked, number of all tracked signals

## Slide 7: Solution Page
PVT Solution Plot Selection:
Pos ENU or Pos Horiz
PVT Solution Plot:
Pos E, N, U: position errors east-west, north-south, up-down *1,
# Sats: Number of used/all satellites
or
Position error horizontal *1 (east-west and north-west, horizontal scatter plot)
Show Ref Pos
Dialog Button
PVT Solution Clear Button
Time Span and Y-axis Range Selections
Ref Pos Dialog
*1 The reference position is automatically selected from the first epoch solution.
It can be modified by using Ref Pos Dialog
Current Solution and Number of Used/All Satellites

## Slide 8: Log Page
Receiver Log Type Selection:
Blank: all log
Receiver Logs *1 *2
Additional Receiver Log Filter:
filter string, like G01 or L1CA, separated by spaces, | indicates OR condition
(e.g., G10|G02|G03)
Receiver Log Pause Button
Receiver Log Clear Button
*1 Refer p.14 for the receiver log formats
*2 To copy the logs to Clip-board, push Pause button, select the logs and push Ctrl-C of the keyboard

## Slide 9: Input Options Dialog
Input Source Selection:
RF Frontend or IF Data
RF Frontend Type Selection:
Currently, only Pocket SDR FE is selectable
USB Bus/Port:
To select device in case of multiple devices connected.
If blank, the device is automatically selected.
Device Configuration File:
RF Frontend configuration (MAX2771 register settings for Pocket SDR FE) to be loaded at the receiver started. Check Device Configuration File and fill the file path. If unchecked, the current configuration for the device is used.
IF Data File *1:
IF data file path, if IF Data selected as the input source. The IF data can be captured by pocket_dump or as IF data log of the receiver with tag files.
Time Offset and Scale:
Start time offset and time scale to playback the IF Data.
IF Data File Property *1:
IF Data Format, Sampling Rate, LO frequency, Sampling Type (I or IQ), Number of sample bits for each RF CH. If the tag file exist for the IF data file, these are automatically configured according to the tag file.
*1 Refer p.13 for the IF data file formats

## Slide 10: Output Options Dialog
PVT Solution Output Path:
PVT Solution (NMEA 0183 GNRMC, GNGGA, GNGSA, GxGSV) path *1.
OBS and NAV Data Output Path:
OBS and NAV Data (RTCM 3.4 MSM (MT1077, 1087, 1097, 1117, 1127, 1137 and 1107) with extension and EPH (MT1019, 1020, 1045, 1046, 1044, 1042 and 1041) path *1 *2
Receiver Log Output Path:
Receiver Log Path *1 *3
IF Data Log Output Path:
IF Data Log Path *1 *4,
It is only valid for RF Frontend selected as the input source
Receiver Log Type Selections *3
*1 The output path should be one of the followings.
(1) <local path>: A local file path <local path>. It can contain time keywords replaced by the log start time. Optionally, it can include the file swapping order “::S=<tint>” by the specified interval <tint> (H).
(2) :<port>: TCP server with the port number <port>. The TCP server waits for and accepts the external TCP connection at the port and output data
(3) <addr>:<port>: TCP client with the address <addr> and the port number <port>. The TCP client connects the external TCP server and output data
*2 The output RTCM 3.4 MSM (with extensions) and EPH can be converted to RINEX OBS and NAV by CONVBIN utility included in the Pocket SDR package
*3 Refer p.14 for the receiver log format. The receiver log can be plotted by the Log Viewer pocket_plot.py in the Pocket SDR package
*4 Refer p.13 for the IF data log format. The output format is automatically selected according to the RF Frontend (RAW8, RAW16 or RAW32). The tag file is also generated.

## Slide 11: Signal Options Dialog
GNSS System and Signal Selections:
System: GNSS System,
Satellite No: Satellite number or number range (n-m) separated by , *1
GNSS Signals: Signal IDs to be tracked
RF CH Assignment Options:
RF CH is automatically assigned for signals. To assign signals to specific RF CH(s) manually, use the option as the format <sig>:<ch_list> separated by spaces, where, <sig> is signal ID and <ch_list> is RF CH number list like 1,3,5-7. Additionally, SRCH:<ch_list> can be used to specify signal search CH(s) to shorten the acquisition time.
System | Signal | Signal ID
GPS | L1C/A | L1CA
 | L1C-D | L1CD
 | L1C-P | L1CP
 | L2C-M | L2CM
 | L5-I | L5I
 | L5-Q | L5Q
GLONASS | L1C/A | G1CA
 | L1OCd | G1OCD
 | L1OCp | G1OCP
 | L2C/A | G2CA
 | L2OCp | G2OCP
 | L3OCd | G3OCD
 | L3OCp | G3OCP
Galileo | E1-B | E1B
 | E1-C | E1C
 | E5a-I | E5AI
 | E5a-Q | E5AQ
 | E5b-I | E5BI
 | E5b-Q | E5BQ
 | E6-B | E6B
 | E6-C | E6C
QZSS | L1C/A | L1CA
 | L1C/B | L1CB
 | L1C-D | L1CD
 | L1C-P | L1CP
 | L1S | L1S
 | L2C-M | L2CM
 | L5-I | L5I
 | L5Q | L5Q
 | L5S-I | L5SI
 |  | L5SIV*2
 | L5S-Q | L5SQ
 |  | L5SQV*2
 | L6D | L6D
 | L6E | L6E
System | Signal | Signal ID
BeiDou | B1I | B1I
 | B1C-D | B1CD
 | B1C-P | B1CP
 | B2a-D | B2AD
 | B2a-P | B2AP
 | B2I | B2I
 | B2b-I | B2BI
 | B3I | B3I
NavIC | L1-SPS-D | I1SD
 | L1-SPS-P | I1SP
 | L5-SPS | I5S
 | S-SPS | ISS*3
SBAS | L1C/A | L1CA
 | L5-I | L5I
 | L5-Q | L5Q
Pocket SDR Signal ID Table
*1 For GPS, Galileo, BeiDou, NavIC and SBAS, these satellite numbers are the same as the signal PRN numbers. For GLONASS, use the frequency channel number (FCN) for FDMA signals and satellite slot number for CDMA signals instead separated by /. For QZSS, which has complicated satellite numbering, use SV IDs (1-5, 8, 9) or non-standard code numbers (6, 10) instead as the satellite numbers.
*2 QZSS L5S verification mode signals
*3 Pocket SDR FE currently does not support S-band signals
Link to Detailed GNSS Signal Table

## Slide 12: System Options Dialog
PVT Options Selection:
Epoch Interval (s), Max Epoch Lag (s) and Elevation angle Mask (deg)
Signal Acquisition and Tracking Options Selection:
Correlation Spacing (chip), Non-coherent Integration Time for Acquisition (s), Non-coherent Integration Time for DLL (s), Loop filter bandwidth for DLL, PLL, FLL (wide-band) and FLL (narrow-band) (Hz), Max Doppler Frequency search range (Hz), C/N0 thresholds for signal-lock or signal-lost decision (dB-Hz), Bump-Jump for BOC modulation enabled or disabled.
FFTW Wisdom Path:
FFTW wisdom file path to shorten the signal acquisition time. The file can be generated by the utility fftw_wisdom in the Pocket SDR package.

## Slide 13: IF Data File Formats
I1
I2
I3
I4
I1
I2
I3
I4
I1
I2
I1
I2
I1
I2
I1
I2
I3
I4
I5
I6
I7
I8
I1
I2
32 bits / sample
16 bits / sample
8 bits / sample
16 bits / sample
8 bits / sample
Ii (int8)
Qi (int8) *1
Ii (int8)
Qi (int8) *1
Ii (int8)
Ii (int8)
Ii (int8)
Ii (int8)
...
I1
Q4
Q2
I2
Q1
I4
Q3
I3
Q6
I6
Q5
I5
Q8
I8
Q7
I7
I1
Q4
I1
Q4
INT8 (int8) *2
INT8X2 *2
(interleaved int8)
RAW8
(FE 2CH raw)
RAW16
(FE 4CH raw)
RAW32
(FE 8CH raw)
Q2
I2
Q1
I1
Q2
I2
Q1
I1
Q2
I2
Q1
I1
Q2
I2
Q1
I1
...
Q2
I2
Q1
I4
Q3
I3
Q2
I2
Q1
I4
Q3
I3
...
...
...
: i-CH I-sample, : i-CH Q-sample
Ii
Qi
MSB
LSB
bits | 00 | 01 | 10 | 11
I | +1 | +3 | -1 | -3
Q *1 | -1 | -3 | +1 | +3
2 bits IQ-sampling
*1 Polarity inverted due to MAX2771 convention
*2 Quantized values only supported in the range [-7 ... +7]
bits | **00 | **01 | **10 | **11
I | +1 | +3 | -1 | -3
2 bits I-sampling
bits | 0000 | 1000 | 0001 | 1001 | 0010 | 1010 | 0011 | 1011
I | +1 | +3 | +5 | +7 | -1 | -3 | -5 | -7
3 bits I-sampling
PROG = Pocket SDR
TIME = 2024/11/01 20:48:00.776 (Start Time GPST)
FMT = RAW16 (Format)
F_S = 24 (Sampling Freq. MHz)
F_LO = 1568,1237.8,1176.45,1278.75 (LO Freq. MHz)
IQ = 2,2,2,2 (Sampling, 1:I, 2:IQ)
BITS = 2,2,2,2 (Sampling Bits)
IF Data Tag File (<path>.tag)

## Slide 14: Receiver Logs
$TIME,time,year,mon,day,hour,min,sec,tsys (time info)
$OBS,time,year,month,day,hour,min,sec,sat,code,cn0,pr,cp,dop,lli,fcn (OBS data)
$NAV,time,sat,sig,nerr,size,data (raw NAV data)
$POS,time,year,month,day,hour,min,sec,lat,lon,hgt,Q,ns,stdn,stde,stdu,dtr (position solution)
$SAT,time,year,month,day,hour,min,sec,sat,pvt,obs,cn0,az,el,res (satellite info)
$EPH,time,sat,sig,IODE,IODC,SVA,SVH,Toe,Toc,Ttr,A,e,i0,OMEGA0,omega,M0,delta-n,OMEGAdot,Idot,Crc,Crs,Cuc,Cus,Cic,Cis,Toes,Fit,Af0,Af1,Af2,
TGD,code,flag (GPS/Galileo/QZSS/BeiDou/NavIC decoded ephemeris)
$EPH,time,sat,sig,tb,fcn,SVH,SVA,age,Toe,Tof,pos-x,pos-y,pos-z,vel-x,vel-y,vel-z,acc-x,acc-y,acc-z,tau-n,gamma-n,delta-tau-n (GLONASS
decoded ephemeris)
$CH,time,ch,rfch,sat,sig,prn,lock,cn0,coff,dop,adr,ssync,bsync,fsync,rev,srev,err_phas,err_code,tow_v,tow,week,type,nnav,nerr,nlol,nfec
(receiver channel info)
$LOG,time,message (error, warning, general info message)
$CH
time receiver time (s)
ch receiver channel number
rfch RF channel number
sat satellite ID
sig signal ID
prn PRN number
lock lock time (s)
cn0 C/N0 (dB-Hz)
coff code offset (ms)
dop Doppler frequency (Hz)
adr accumlated Doppler range (cyc)
ssync secondary code sync flag(0:async,1:sync)
bsync symbol/bit sync flag (0:async,1:sync)
fsync frame sync flag (0:async,1:sync)
rev primary code polarity (0:normal,1:reversed)
srev secondary code polarity (0:normal,1:reversed)
err_phas phase error (cyc)
err_code code error (10^-6 s)
tow_v tow valid flag (0:invalid,1:valid,
2:ambiguity unresolved)
tow time of week (ms)
week week number (week)
type navigation subframe or message type
nnav navigation subframe/message count
nerr error subframe/message count
nlol loss-of-lock count
nfec number of error corrected (bits)
$SAT
time receiver time (s)
year,month,day solution day (GPST)
hour,min,sec solution time (GPST)
sat satellite ID
pvt PVT status (0:not used,1:used)
obs L1 obs data status
(0:unavailable,1:available)
cn0 L1 signal C/N0 (dB-Hz)
az azimuth angle (deg)
el elavation angle (deg)
res L1 pseudorange residual (m)
$EPH
time receiver time (s)
sat satellite ID
sig signal ID
... decoded ephemeris parameters
$LOG
time receiver time (s)
message error, warning or general
info message
$TIME
time receiver time (s)
year year (2000-2099)
mon month (1-12)
day day (1-31)
hour hour (0-23)
min minute (0-59)
sec second (0.000-59.999)
tsys time system (GPST or UTC)
$OBS
time receiver time (s)
year,month,day
obs data day (GPST)
hour,min,sec
obs data time (GPST)
sat satellite ID
code RINEX obs code
cn0 C/N0 (dB-Hz)
pr pseudorange (m)
cp carrier phase (cyc)
dop Doppler frequency (Hz)
lli loss-of-lock indicator
fcn frequency channel number
for GLONASS FDMA signals
$NAV
time receiver time (s)
sat satellite ID
sig signal ID
nerr number of corrected error
bits
size raw NAV data size (bits)
data raw NAV data HEX dump
$POS
time receiver time (s)
year,month,day solution day (GPST)
hour,min,sec solution time (GPST)
lat solution latitude
(deg,+:north,-:south)
lon solution longitude
(deg,+:east,-:west)
hgt solution ellipsoidal height
(m)
Q quality flag (=5: single)
ns number of valid satellites
stdn solution standard-dev north
(m)
stde solution standard-dev east
(m)
stdu solution standard-dev up (m)
dtr receiver clock bias (s)